## Slide 1: Components of a Processor
Switches, Gates, and Some History
© 2018 L. V. Kale at the University of Illinois Urbana-Champaign

## Slide 2
To be able to effectively program a modern multiprocessor, we have to understand what it is made up of and how it came to be the way it is today

## Slide 3: What Are Computers Made of?
Building blocks of computers
Why has frequency scaling stalled?
Conception of parallel computing
Machine organization
……..
Complexity of modern processors makes performance oriented programming challenging

## Slide 4: A Computer today is a powerful machine
We have been able to make a “machine” that can do complex things
    Weather forecast, design of medicinal drugs
    Speech recognition, robotics, artificial intelligence
    Web browsers, Internet communication protocols
What is this machine based on?

## Slide 5: The Modest Switch
All these capabilities are built from an extremely simple component:
  A controllable switch
The usual electrical switch we use every day
  Turns current on and off
  But we need to turn it on and off by hand
The controllable switch
  Voltage controls if the switch is on or off
  High voltage at input: switch on
    Otherwise it is off

## Slide 6: Let’s Use Them Creatively
Output is high if both input1 AND input2 are high
If either of the inputs is low, the output is low
Input1
Input2
Output
This is called an AND gate
Now, can you make an OR gate with switches?

## Slide 7: OR Gate
Input1
Input2
Output
Output is high if either Input1 OR input2 (or both) is high

## Slide 8: Basic Gates
There are three basic kinds of logic gates
AND
of two inputs
OR of two inputs
NOT
(complement)
on one input
Operation:
Logic gate:
Two questions:
  How can we implement such switches?
  What can we build with gates?
    Adders, controllers, memory elements, computers!

## Slide 9: You Can Make an Adder with Gates
xor
Full adder (with carry)
4 bit adder

## Slide 10: How About Some Memory?
Switches help us build memory
How can a circuit “remember” anything on its own?
  After all, the values on the wires are always changing, as outputs are generated in response to inputs
The basic idea is feedback: we make a “loop” in the circuit, so the circuit outputs are inputs as well
When S and R are 0, Q is “stable”: whatever it was, it stays in that state
Ergo: memory
When S is 1 and R is 0, Q becomes 1
When R is 1 and S is 0, Q becomes 0
Set and reset inputs…

## Slide 11
Instruction Memory
PC (Program Counter)
ALU
Data Memory
Components of a Stored-Program Computer
Instruction
Move to the next location
Register set

## Slide 12
How computers are built from switches/gates is a matter for other courses
For this course, remember:
Computers are made from some very simple components by putting a large number of them together in interesting ways, and running them really fast
Notes: End Video Here.