## Slide 1: Memory Access Challenges
Introduction to Caches
© 2018 L. V. Kale at the University of Illinois Urbana-Champaign

## Slide 2: Components of a Stored-Program Computer
Instruction Memory
PC (Program Counter)
CPU
Data Memory
Instruction
Register name
Data
Move to the next location
Register set

## Slide 3: Latency to Memory
Data processing involves transfers between data memory and processor registers
DRAM: large, inexpensive, volatile memory
  Latency: ~50ns
    Comparatively slow improvement over time: 80 -> 30 ns
  A single core clock is 2 GHz: it beats twice in a nanosecond!
    Can perform upward of 4 ALU operations/cycle
  Modern processors have tens of cores on a single chip
  Take away:
    Memory is significantly slower than the processor

## Slide 4: Bandwidth Can Be Increased
More pins can be added to chips
3D stacking of memory can increase bandwidth further
  Need methods that translate latency problems to bandwidth problems
  Solution: concurrency
  Issues:
    Data dependencies

## Slide 5: Cache Hierarchies and Performance
CPU
Memory
Cache
Cache is fast memory, typically on chip
  DRAM is off-chip
It has to be small to be fast
It is also more expensive than DRAM on per-byte basis
Idea: bring frequently accessed data in the cache

## Slide 6: Why and How Does a Cache Help?
Temporal and spatial locality
  Programs tend to access the same and/or nearby data repeatedly
Spatial locality and cache lines
  When you miss, you bring not just the word that CPU asked for, but a bunch of surrounding bytes
  Take advantage of the high bandwidth
  This “bunch” is a cache line
  Cache lines may be 32-128 bytes in length
Notes: 6

## Slide 7: Cache Hierarchies and Performance
Memory
CPU
Memory
Cache
CPU
Caches

## Slide 8: Some Typical Speeds/Times Worth Knowing
 | Latency | Bandwidth
Modern processor |  | 
L1 cache |  | 
L2-L3 cache |  | 
DRAM |  | 
Solid state drive |  | 
Hard drive |  | 
Network: Cluster |  | 
Network: Ethernet |  | 
Network: World-wide-web |  | 

## Slide 9: Some Typical Speeds/Times Worth Knowing
 | Latency | Bandwidth
Modern processor | 0.25 ns | 
L1 cache | several ns | 
L2-L3 cache | 10s ns | 
DRAM | 30-70 ns | 10-20GB/s
Solid state drive | 0.1ms | 200-1500 MB/s
Hard drive | 5-10 ms | 200MB/s
Network: Cluster | 1-10 µs | 1-10GB/s
Network: Ethernet | 100 µs | 1GB/s
Network: World-wide-web | 10s of ms | 10Mb/s (note b vs. B)

## Slide 10: Architecture Trends: Pipelining
Architecture over 2-3 decades was driven by the need to make clock cycle faster
  Pipelining developed as an essential technique early on
  Each instruction execution is pipelined:
    Fetch, decode, execute, stages at least
    In addition, floating point operations, which take longer to calculate, have their own separate pipeline
  So, no surprise: L1 cache accesses in Nehalem are pipelined
    Even though it takes 4 cycles to get the result, you can keep issuing a new load every cycle, and you wouldn’t notice a difference (almost) if they are all found in L1 cache (i.e., are “hits”)