## Slide 1: Cost Model
© 2018 L. V. Kale at the University of Illinois Urbana

## Slide 2: A simple cost model for message passing
Messaging cost is α + n*β , where
  α : per message cost
  β : Per byte cost
For the sake of intuition:
  Assume α is 1,000 times larger than β
  Typical: per message cost may be 1 microsecond on a supercomputer, and tens of microseconds on commodity clusters,
    Per byte cost may be 1 ns (corresponds to 1 Gbyte/s, not Gbit/s, bandwidth)
What do we mean by “messaging cost”
  Latency
  Overhead to Processor

## Slide 3: Communication Cost Model
This model ignores several factors:
  It assumes there is no contention in the network
  It assumes latency is independent of distance
    Which is mostly true, in no-contention scenario
  We will revisit these issues when we study network topologies
    But note that for first-order analysis, the α + n*β model is good enough
  Also, it ignores packetization and per-packet overheads

## Slide 4: Communication co-processor and CPU overhead
CPU overhead: how much time is taken away from the CPU to deal with communication
  Function calls
  Data copying, if needed
  Setup / interaction with the network
  In MPI: tag matching
Using a co-processor (a modern NIC will do) ”off-loads” some of the communication work from the CPU
  Especially explicit data copying, in many cases
For this reason, it is useful to separate overhead and latency

## Slide 5: Communication Basics: Point-to-point
Sending processor
Sending co-processor
Network
Receiving co-processor
Receiving processor
Each component has a per-message cost, and per byte cost
Each cost, for a n-byte message
  = ά + n β
Important metrics:
  Overhead at processor, co-processor
  Network latency
  Network bandwidth consumed
    Number of hops traversed
Notes: 5

## Slide 6: Communication Basics
Message Latency: time between the application sending the message and receiving it on the other processor
Send overhead: time for which the sending processor was “occupied” with the message
Receive overhead: the time for which the receiving processor was “occupied” with the message
Network latency
Separating overhead in analysis is useful only when you are using the time until communication completes for some computation, or for setting up another communication
  Example: consider cost of sending 10 messages to 10 distinct processors
    The overheads are serialized on the CPU, the latencies are overlapped
Except when we state otherwise, we will use the simple α + n*β model without separating overhead

## Slide 7: Overall Cost Model
Execution time (aka completion time) can be modeled, for many applications, as communication cost
  T= Tcomp + Tcomm
This assumes
  All processes are doing the same work
  There is no overlap of communication and computation
  With Overlap, T= Tcomp + Tcomm - Toverlap
Do this for
  Each processor (if they are doing the same thing)
  Worst loaded processor, if the loads are imbalanced, or
  longest chain (critical path) if that dominates
Typically, to get the completion time expression

## Slide 8: Other models: LogP, logGP, etc.
LogP is an acronym: L: Latency, o: overhead, g: gap, p: processors
  g : time period for injecting a short fixed size message
    Maybe accounts for bandwidth, or contention or injection rate
  Model is meant for theoretical analysis of algorithms with short fixed-size messages
LogGP: generalized to arbitrary size messages
  Starts resembling α + n*β model, as long as we take cognizance of overhead
My advice:
  Write (i.e. model) completion time expression, phase-by-phase if possible, with α + n*β model,
    keeping in mind the characteristics of algorithm (critical path? Load balance? Overlap?)
  Always measure, and compare with model

## Slide 9: Cost Model: Examples
Stencil, Gauss-Seidell
© 2018 L. V. Kale at the University of Illinois Urbana

## Slide 10: Gauss-Jacobi Relaxation
while (maxError > Threshold) {
Re-apply Boundary conditions
maxError = 0;
for i = 0 to N-1 {
for j = 0 to N-1 {
B[i,j] = 0.2 * (A[i,j] + A[i,j-1] +
A[i,j+1] + A[i+1, j] + A[i-1,j]) ;
if (|B[i,j]- A[i,j]| > maxError)
maxError = |B[i,j]- A[i,j]|
}
}
swap B and A
}
Sequential Pseudocode:
Decomposition by:
Row
Blocks
Or Column

## Slide 11: Performance Estimate
Computation, Tcomp , is tc* N*N/p, where tc is the computation cost per cell
  For either decomposition
Communication cost: Tcomm
  For Row decomposition: 2 messages of size N words (of 8 bytes each)
    2*(α + 8*N *β )
  For tile decomposition: 4 messages of size N/sqrt(p) words (of 8 bytes each)
    4*(α + 8*N *β/(sqrt(p) )
  Which one is better? Compare for specific values of N, p, α , and β

## Slide 12: Gauss-Seidel Relaxation
While (maxError > Threshold) {
Re-apply Boundary conditions
maxError = 0;
for i = 0 to N-1 {
for j = 0 to N-1 {
old = A[i, j]
A[i, j] = 0.2 * (A[i,j] + A[i,j-1] +A[i,j+1]
+ A[i+1,j] + A[i-1,j]) ;
if (|A[i,j]-old| > maxError)
maxError = |A[i,j]-old|
}
}
}
Sequential Pseudocode:
No old-new arrays..
Sequentially, how well does this work?
It works much better!
How to parallelize this?

## Slide 13: How Do We Parallelize Gauss-Seidel?
Visualize the flow of values
Not the control flow:
  That goes row-by-row
Flow of dependences: which values depend on which values?
Does that give us a clue on how to parallelize?

## Slide 14: Parallelizing Gauss-Seidel
Some ideas
  Row decomposition, with pipelining
  Square over-decomposition
    Assign many squares to a processor (essentially same?)
PE0
PE1
PE2
PEp-1
…

## Slide 15
N
N
W
N/P
# Columns = N/W
# Rows = P
1
1
2
2
2
2
...
...
...
P
...
...
...
P
P
P
# Of Phases
P
P
P
P
...
...
...
...
...
...
...
...
...
...
...
...
N
W
N
W
N
W
N
W
N
W
N
W
N
W
N
W
N + 1
W
N + 1
W
...
N + 1
W
N + 1
W
...
N + 1
W
+1
N/W
+P-1
+ (P-1)
Row decomposition with pipelining
Notes: Slide done by eric shook

## Slide 16
Time
Number of Procs Used
P
0
P
N
W
N + P -1
W
  Row decomposition, with pipelining

## Slide 17: Apply the cost model to Gauss-Seidel
Apply the cost model to Gauss-Seidel, and then find the optimal w
Completion time:
  Sum of 3 phases: rising, plateau, falling phase
  Communication in each phase is 1 message of W words:

## Slide 18: Red-Black Squares Method
Red squares calculate values based on the black squares
  Then black squares use values from red squares
  Now red ones can be done in parallel, and then black ones can be done in parallel
A “square” may be just a single point
  Or it can be a kxk tile of values
    Each tile locally can do Gauss-Seidel computation
    Faster convergence of Gauss-Seidel