## Slide 1: Interconnect Topologies
Understanding using the communication infrastructure
© 2018 L. V. Kale at the University of Illinois Urbana

## Slide 2: Shared Memory
PE0
PE1
PEN
Memory
PE2
Is anyone in charge of a part of memory?
Is there a notion of relative proximity?
NO
No
May be: NUMA

## Slide 3: Not entirely true!
PE0
PE1
PEN
Memory
PE2
Some part(s) of memory may be closer than others
What kind of network?
Network
Bus
Switch

## Slide 4: Distributed Memory Systems
PE0
Mem0
Others
PE1
Mem1
Others
PE2
Mem2
Others
PEp
Memp
Others
Locality of data is exposed
But beyond that…

## Slide 5: Distributed Memory Systems
node0
core0, c1,c2, ..
Mem0
Others
Mem1
Others
Mem2
Others
Memp
Others
Locality of data is exposed
But beyond that…
node1
core0, c1,c2, ..
nodep
core0, c1,c2, ..
node2
core0, c1,c2, ..

## Slide 6: Programmer’s View
Rest of the System
How is the rest of the system connected?
Why do I care?
Ring, Star, Butterfly, Mesh, Torus, Tree..
PERFORMANCE
node0
core0, c1,c2, ..
Mem0
Mem1
Mem2
Memp
node1
core0, c1,c2, ..
node2
core0, c1,c2, ..
nodep
core0, c1,c2, ..
NIC
NIC
NIC
NIC

## Slide 7: Why Think About Interconnect Topologies?
If you are a machine designer: cost, average application performance, hot-spots
  Same considerations if you are a buyer of such machines
  Consider the mix of applications your users run
    Because interconnect choices impact different applications differently
If you are an application programmer:
  Which of the available machines to use?
  How to optimize performance on a given topology

## Slide 8: Commonly Discussed Network Topologies
Butterfly
Commonly Discussed Network Topologies

## Slide 9: Commonly Discussed Network Topologies
1-D torus (ring)
1-D Mesh
Ternary Tree
Fully connected
Star graph

## Slide 10: Commonly Discussed Network Topologies
2-D Mesh
2-D Torus
3-D Mesh
3-D Torus
You can avoid long wires by laying out each line this way

## Slide 11: Commonly Discussed Network Topologies
Hypercubes

## Slide 12: Commonly Discussed Network Topologies IBM’s PERCS
PERCS: Multi-tier all-to-all
Diagram by Abhinav Bhatele

## Slide 13: Basic Topology requirements
For things to work
  Must connect each processor to all others. i.e. it should be possible to send “messages” between any pair of processors
  Must allow for physically viable arrangements (try arranging a star for thousands of processors)
  The physically viable arrangement should be economically affordable

## Slide 14: Basic Topology requirements
For things to work well:
  Intermediate routing, if needed, should happen without interfering with computation on intermediate nodes.
  Reasonable path length between every pairs of processors
  Easy to calculate path from one processor to other
  More discussed later…

## Slide 15: Interconnect Topologies
Metrics for analyzing network topologies
© 2018 L. V. Kale at the University of Illinois Urbana

## Slide 16: Topology Basic definitions
Let the topology be represented by a Graph G(V,E) where V is the set of vertices - processors/routers and E is the edges - connections among them
degree: maximum number of edges incident on a vertex
distance between two vertices: number of edges (hops ) in shortest path between them
diameter: maximum distance between any pair of vertices
edge length : maximum physical length of any wire; may be constant or variable as number of processors varies
bandwidth

## Slide 17: How to Judge a Topology
degree: affects capability to communicate simultaneously
diameter: determines the maximum delay
average distance
link bandwidth L: impacts how fast communication is done
Bisection bandwidth
  Divide the set of processors in two equal partitions – many possible partitions
  How much link bandwidth is available for data flow from one partition to the other?
  Take the smallest (worst) value over all possible partitions
  Important for global communication, congestion
All-to-all bandwidth:
  How many bytes get transferred per unit time if every process is sending a m byte message to every other process
  Bisection bandwidth is an upper bound (often tight) on all-to-all bandwidth

## Slide 18: Fully Connected Network
degree:
diameter:
average distance
total number of links :
bisection bandwidth:
What if everyone wants to send data to every one else?
Does this look like an overkill?
P-1
1
L.P.P/4
1
P(P-1)/2

## Slide 19: Chains
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
Single point of failure!
Asymmetric – not a good idea
1-2
P-1
L
P/3
P-1

## Slide 20: Rings (k-ary 1-cube, or wrapped chain)
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
What if everyone wants to send data to every one else?
2
P/2
2L
P/4
P

## Slide 21: 2D Meshes (say P = k * k)
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
Asymmetric – not good!
Bisection bandwidth is tolerable
2-4
2(k-1)
kB
2k/3
2k(k-1)

## Slide 22: 2D Torus (k-ary 2-cube)
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
4
k-1
2kL
k/2
2k*k

## Slide 23: k-ary n-cube : generalization of Torus
P = k * k * k *…. Or P = k1 * k2 * k3 * ….
Degree = 2n
Diameter = n*k/2
Average Distance = n*k/4
Bisection Bandwidth = 2L*P/k

## Slide 24: Hypercubes: Binary n-cubes
Hypercubes
Dimension d (aka n, hence the name n-cube), number of nodes N = 2n
Diameter: d = n
Bisection bandwidth: wN/2

## Slide 25: Why did Hypercubes Die?
Disadvantages of hypercube?
  Wire lengths? May span the entire machine
    Leads to reduced bandwidth per link, unless its optical
    Copper vs optical interconnects:
      Copper is cheaper but constrained by length
  Number of connections per node increases with the size of the machine
K-ary n-cube allows one to seek intermediate points between meshes and hypercubes.
  N-dimensional “hyper” cube, but number of processors along each dimension is k (instead of 2 of binary hypercube)
But they are making a comeback
  HPE’s Eagle system at NREL

## Slide 26: Interconnect Topologies
Fat Trees, Moore Graphs, networks with high radix switches
© 2018 L. V. Kale at the University of Illinois Urbana

## Slide 27: Trees
Diameter and average distance are logarithmic
-k-ary tree, height logk P, diameter = 2 logk P
Fixed degree k.
Low bisection bandwidth = L for binary trees.
  Exercise: analyze ternary trees for bisection bandwidth and all-to-all bandwidth

## Slide 28: Fat Trees
Fatter higher bandwidth links (more connections in reality)
Bisection width scales with number of nodes N
We will return to this idea later

## Slide 29: Are Hypercubes optimal? Moore Graphs
Moore bound: given degree d and diameter k, the largest number of vertices a graph can have is:
Conversely, given n vertices, and degree d, the best diameter we can hope for is: k = log(d-1)(n)
Given n = 1000, d = 10, k >= 4
A Moore graph of degree d and diameter k is one that achieves the Moore bound above
1 3 6 12…

## Slide 30: Known Moore graphs
Peterson Graph: 10 vertices, degree = 3, diameter = 2.
Singleton graph: 50 vertices, degree = 7, diameter = 2
A 3rd graph might possibly exist, of degree 57!

## Slide 31: Low Diameter (LD) Graphs
So, Moore graphs won’t help us much, directly, because there are only 2 of them
But it inspires us to look at graphs with diameters close to the Moore bound and better than hypercube’s log2 p diameter
Such graphs are useful also as “soft” structures in parallel algorithms
  E.g. diffusive load balancing
  Build a communication pattern along a LD graph, and diffuse load along those neighbors, irrespective of interconnect topology
How to construct them?
  Many systematic ways
  Also, randomly generated graphs tend to be LD graphs!

## Slide 32: Interconnect Topologies
Networks with high radix switches
© 2018 L. V. Kale at the University of Illinois Urbana

## Slide 33: Switches and Indirect networks
switch
switch
switch
Terminal
switch
Direct networks: 1 switch at each node
Indirect networks: Switches connect to (internal) switches
Multiple nodes connected to many “terminal” switches
node
node
node
switch
switch

## Slide 34: Butterfly
For P processors, log p ranks with p switches
Node(i,j) is connected to two nodes with rank i-1 – node(i-1,j) and node(i-1,m) where m is the integer found by flipping the ith most significant bit in binary representation of j
Rank 3 vertices can be processors/memory
© 2016 Sachingf / CC BY-SA 4.0 / https://goo.gl/5PXsuh

## Slide 35: Fat Tree/Clos Topology
a)
b)
c)
4-ary 1-tree
4-ary 2-tree
4-ary 3 tree
Only a small subset of connections at this level are shown

## Slide 36: Fat Trees/Clos with modern switches
Routing:
  Go up via random path to the highest level switch (or lowest common ancestor), and follow a deterministic path from there to your destination
For many years now, the number of ports a high-end switch can support (i.e. its “radix”) has been rising
  E.g. 32 or 48 ports are relatively common
  This has made it possible to design Fat Trees with a height of just 3 or 4
Another idea is to use expensive very high radix “Core” switches
  E.g. Lonestar supercomputer at TACC, with 1,888 nodes
    4 Mellanox IS5600 648-port core switches at the higher level
    118 chassis switches (16x16) at the lower level
    16 nodes connected to each chassis switch, which connects 4 links to each core switch
    3 hops max from any node to any other node

## Slide 37: IBM’s PERCS (direct) network
Each supernode includes 32 nodes that are fully connected
  Each node has a switch with 31 (L) links for within-supernode connections, and 16 optical (D) for connections to other supernodes
  3 hops to go from any node to any other: diameter 3!
Optional more info: http://spcl.inf.ethz.ch/Publications/.pdf/ibm-percs-network.pdf

## Slide 38: IBM’s PERCS network

## Slide 39: IBM’s PERCS network
Very high bisection bandwidth on the full machine
  Illinois’ original* blue waters design based on PERCS would have had several hundred supernodes (but fewer than max 512 allowed by the topology)
A problem:
  If you are running a job on a small fraction of the machine (but more than 32 nodes, so it can’t fit within a supernode)
  A natural allocation is to use the smallest number of supernodes that will accomodate the job
    But this leads to bad bisection bandwidth
    Consider 64 nodes allocation on 2 supernodes.. Only 1 (optical) link between the 2!
  Solutions:
    Randomized allocation (spread the 64 nodes over many supernodes), OR
    Indirect routing (send a message to a random supernode first)
    Optional reading: Bhatele et al, SC’11. Hoefler & Snir, ICS ‘11
* Eventually, Illinois’ Blue Waters was built by Cray using a 3D torus network

## Slide 40: Cray’s Aries Interconnect
Two level network:
The Electrical group includes nodes connected in 2 hops via a collection of switches
These groups (akin to the supernode) are fully connected by optical links
  i.e. one hop to go from any supernode to any other, as long as you are on the right node
Direct route: 5 hops max
PERCS, Aries etc. can be generalized as “Dragonfly” class of topologies

## Slide 41: Summary: ``Direct” networks
Name | parameter/s & relationship with p | Degree | Diameter | Bisection Bandwidth | Wire lengths
Chain |  | 2 |  | L | short
Ring |  | 2 |  | 2L | short
2D mesh | k, p = k2 | 4 | 2(k-1) | kL | short
2D torus | k, p = k2 | 4 | k | 2kL | short
3D mesh | k, p = k3 | 6 | 3(k-1) | k2L | short
3D torus | k, p = k3 | 6 | 3k/2 | 2k2L | short
n-D mesh, n>3 | k, n: p = kn | 2k | n(k-1) | k(n-1)L | variable
n-D torus (k-ary n-cube) | k, n: p = kn | 2k | nk/2 | 2k(n-1)L | variable
Binary ncube (hypercube) | d = log2 p | d | d | pL/2 | variable
PERCS | S = 512 supernodes | 47 | 3 (or 5) | s2 L/2 | Variable
p : number of nodes
L: link bandwidth
k, n : topology specific parameters; make it easy to express other properties concisely

## Slide 42: Interconnect Topologies
How to Deal with a Given Network Topology
© 2018 L. V. Kale at the University of Illinois Urbana

## Slide 43: Dealing with the Interconnect
As a programmer, you become aware of the network if your program suffers from unexpected communication delays
  Where expected delays are thos predicted by the 𝛂 + n 𝛃 formula, with no-load machine-specific values of 𝛂 and 𝛃
  This indicates contention in the network
What to do if contention is cause of significant performance loss?
  Map ranks to physical nodes so that communicating processes are nearby
    Messages occupy fewer wires, reducing congestion
    Useful to have a variable as a communicator, rather than MPI_COMM_WORLD
    You can create a new communicator based on communication patterns
    Need physical topology information as well as communication profile
  Other techniques:

## Slide 44: Technique 1: Remapping ranks
Map ranks to physical nodes so that communicating processes are nearby
  Messages occupy fewer wires, reducing congestion
  Useful to have a variable as a communicator, rather than MPI_COMM_WORLD
  You can create a new communicator based on communication patterns
  Need physical topology information as well as communication profile
Tools for this exist
  Or write your own

## Slide 45: Technique 2: Let the runtime handle mapping
Let the runtime handle mapping
  Charm++ and AMPI
  Experss communication graph, and exploit the pattern at runtime to remap objects or ranks to physical resources
  Need load balancers that are topology aware

## Slide 46: Technique 3: spread communication
Bursty communication, when all processes strat injecting messages over a short fraction of the application timestep (typically, in sync), should be avoided
Over-decomposition naturally achieve that
  Charm++ or AMPI
  Alternatively, manual over-decomposition to spread injection of messages over timestep or iteration

## Slide 47: Things to explore
Which network suits which type of communication?
Find the networks used in modern machines – Mira, Blue Waters, Stampede, Tianhe, K computer, Summit,
How does one embed one topology in another topology?
How would you connect processors?