## Slide 1: GPGPUs: Overview
Pedagogically precursor concepts
© 2018 L. V. Kale at the University of Illinois Urbana-Champaign

## Slide 2: Precursor Concepts: Pedagogical
Architectural elements that, at least pedagogically, are precursors to understanding GPGPUs
  SIMD and vector units.
    We have already seen those
  Large scale “Hyperthreading” for latency tolerance
  Scratchpad memories
  High Bandwidth memory

## Slide 3: Tera MTA, Sun UltraSPARC T1 (Niagara)
Tera computers, with Burton Smith as a co-founder (1987)
  Precursor: HEP processor (Denelcor Inc.), 1982
First machine was MTA
  MTA-1, MTA-2, MTA-3
Basic idea:
  Support a huge number of hardware threads (128)
    Each with its own registers
  No Cache!
  Switch among threads on every cycle, thus tolerating DRAM latency
  These threads could be running different processes
  Such processors are called “barrel processors” in literature
    But they switched to the “next thread” always.. So your turn is 127 clocks away, always
Was especially good for highly irregular accesses

## Slide 4: Scratchpad memory
Caches are complex and can cause unpredictable impact on performance
Scratchpad memories are made from SRAM on chip
  Separate part of the address space
  As fast or faster than caches, because no tag-matching or associative search
  Need explicit instructions to bring data into scratchpad from memory
  Load/store instructions exist between registers and scratchpad
Example: IBM/Toshiba/Sony cell processor used in PS/3
  1 PPE, and 8 SPE cores
  Each SPE core has 256 KiB scratchpad
  DMA is mechanism for moving data between scratchpad and external DRAM

## Slide 5: High Bandwidth Memory
As you increase compute capacity of processor chips, the bandwidth to DRAM comes under pressure
  Many past improvements (e.g. Intel’s Nehalem) were the result of improving bandwidth, including integration of memory related hardware into processor chip
  Recall: Bandwidth is a matter of resources (here with some inherent limits on number of pins per chip)
  GPUs have historically used higher bandwidth DRAM configurations
    GDDR3 SDRAM, GDDR4, GGDR5, GGDR5X (10-ish Gbits/s per pin)
Recent advance: High Bandwidth memory via 3D stacking
  Multiple DRAM dies are stacked vertically and connected through-silicon vias (tsv)
  NVIDIA,
  MCDRAM (Intel), Hybrid Memory Cube (Micron)

## Slide 6: GPGPUs
General Purpose Graphics Processing Units (GPUs)
© 2018 L. V. Kale at the University of Illinois Urbana-Champaign

## Slide 7: GPUs and General Purposing of GPUs : I
Graphics Processing Unit (GPU)
  Drive the displays connected to a computer
  Wikipedia: “.[…] designed to manipulate .. memory to accelerate creation of images in a frame buffer.”
  Original purpose: high speed rendering i.e. video games, etc.
Due to need for speed in usages like video games, there was pressure to increase their speed and capabilities
  Especially in the 1990’s with the rise of 3D graphics
  Helped along by APIs of OpenGL, DirectX, Direct3D
  Nvidia’s GeForce 3 had enough hardware support to do programmable shading

## Slide 8: GPUs and General Purposing of GPUs : II
GPGPUs were dedicated units, with a specialized function, but
  They were getting faster and faster
  They were getting more programmable in order to support graphics capabilities
Many individuals and researchers in high performance computing started noticing that these devices could be used for computations
  At least for a few, but commonly needed, patterns, such as data parallel loops!

## Slide 9: GPUs and General Purposing of GPUs : III
Graphics Processing Unit (GPU)
Original purpose: high speed rendering(?) i.e. video games, etc
Optimized for being good at math
Result: High memory BW and many “cores”
Brook Streaming Language from Stanford
  Ian Buck et al paper is worth a read
  The idea of specialized kernels
    Running on specialized devices
NVIDIA and AMD (and Intel’s integrated graphics)
Programming: CUDA, OpenCL, and OpenMP
In this paper, we present Brook for GPUs, a system for general-purpose computation on programmable graphics hardware. Brook extends C to include simple data-parallel constructs, enabling the use of the GPU as a streaming coprocessor.

## Slide 10
Holds Global Memory and Constant Memory
Schematic GPGPUs
Each SM is like a Vector Core
SM
SM
SM
Cache for Constant Memory
Fast DRAM
GPGPU Chip
ALU
Registers
Streaming Multiprocessor
Warps
Scratchpad Memory
AKA Shared Memory
The Device

## Slide 11
Holds Global Memory and Constant Memory
Schematic GPGPUs
Each SM is like a Vector Core
SM
SM
SM
Cache for Constant Memory
Fast DRAM
ALU
Registers
SM
Warps
Scratchpad Memory
GPGPU Chip

## Slide 12: CPU vs GPGPU Comparison
CPU (Host)
Latency optimized
10s of Cores
10s of Threads
Memory
Cache hierarchy
Perf. via fast memory/large caches
GPU (Device)
Throughput optimized
1000s of “Cores” (CUDA cores)
10,000s of Threads
Memory (on board)
Simplified cache
  No cpu-like consistency support
Perf. via massive (regular) parallelism

## Slide 13: SIMT
Single Instruction Multiple Threads
Programming Model
Execution Model
Control
ALU
Control
ALU
Control
ALU
Control
ALU
ALU
ALU
ALU
Control
ALU

## Slide 14: Memory
Separate
Fast
Types
  Registers
  Shared v Cache
  Global
  Texture, Read Only, etc
Notes: Delete??

## Slide 15: GPGPU: Programming with CUDA
GPGPU Software Architecture
© 2018 L. V. Kale at the University of Illinois Urbana-Champaign

## Slide 16: CUDA
We will present a very simple, over-simplified, overview
Explicit resource-aware programming
What you specify
  Data transfers
  Data parallel kernel/s, expressed in form of threads
    Each thread does the action specified by the kernel
  The total number of threads are grouped into teams called “blocks”
  Kernel calls specify the number of blocks , and number of threads per block

## Slide 17: Programming Model Overview
Host (serial)
Launches device functions (parallel)
Control can return asynchronously
Memory?
  Device memory
  “Unified” memory
Overlap
  It is possible to overlap data transfer of one kernel with computation of another
Serial
Parallel
Serial

## Slide 18: Simple CUDA Program
#include <stdio.h>
void hello() {
printf(“Hello, world!\n”);
}
int main() {
hello();
}
$ gcc hello.c
$ ./a.out
Hello, world!
Notes: __global__ denotes GPU function aka kernel
<<<>>> denote kernel launch aka running on device

## Slide 19: Simple CUDA Program
#include <stdio.h>
__global__
void hello() {
printf(“Hello, world!\n”);
}
int main() {
hello<<<1,1>>>();
}
$ gcc hello.c
$ ./a.out
Hello, world!
$ nvcc hello.cu
$ ./a.out
Hello, world!
Notes: __global__ denotes GPU function aka kernel
<<<>>> denote kernel launch aka running on device

## Slide 20: Blocks
Basic parallel unit
Threads in a block can assume access to a common shared memory region (scratchpad).
Analogous to processes
Blocks grouped into grid
Asynchronous
int main() {
hello<<<128,1>>>();
}
$ ./a.out
Hello, world!
Hello, world!
…
Hello, world!

## Slide 21: Threads
Sub-division of a block (shared memory)
Analogous to OpenMP threads
Grouped into warps (shared execution)
Level of synchronization and communication
int main() {
hello<<<1,128>>>();
}
$ a./out
Hello, world!
Hello, world!
…
Hello, world!

## Slide 22: Warps
Groupings of threads
All execute same instruction (SIMT)
One miss, all miss
Thread divergence, No-Ops
Analogous to vector instructions
Scheduling unit
Notes: Scheduling picture (+ SIMT picture)

## Slide 23: Combining Blocks, Warps, and Threads
0 | 1 | 2 | 3 | 4 | 5 | 0 | 1 | 2 | 3 | 4 | 5 | 0 | 1 | 2 | 3 | 4 | 5
KernelFunc<<<3,6>>>(…);
Block Dimension = 6
For this picture, assume a warp has 3 threads.. (in reality, its almost always 32.. It’s a device dependent parameter)
If you specify blocksize that’s not a multiple of warpsize, the system will leave some cuda cores in a warp idle)
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
Thread Index
Global Index
Block 1
Block 2
Block 3
Warp 1
Warp 2
Number of Blocks
Number of Threads per Block

## Slide 24: Illustrative Example
__global__
void vecAdd(int* A, int* B, int* C) {
int i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
}
…
int main() {
// Unified memory allocation
vecAdd<<<VEC_SZ/512,512>>>(A, B, C);
}
Number of Blocks
Number of Threads per Block
blockIdx.x is my block’s serial number
blockDim.x is the number of threads per block
threadIdx.x is my thread’s id in my block
VEC_SZ/512
Notes: Non-divisible numbers
These variables are provided by the system to each thread
Block idx is my blocks serial no, blockdim the no of threads per block, treadidx my threads id in my block

## Slide 25: Using OpenMP for GPU programming
A Simpler way of using GPGPUs

## Slide 26: Background: OpenMP support for GPGPUs
Traditional solution: use specialized languages (CUDA/OpenCL)
  Need to rewrite lots of code
  Target only subset of device types
    e.g.: CUDA code can’t run on AMD GPUs, OpenCL is slow on Nvidia
OpenMP 4.0+ has support for offloading computation to accelerators
  Lots of overlap with (earlier) OpenACC standard
    OpenMP already widely used for multicore parallelization
    Mixing OpenACC and OpenMP is difficult
  Can target different types of devices (Nvidia GPUs, AMD GPUs, Xeon Phi, …)
  OpenMP standard only describes interface, not implementation
    Each compiler needs to implement support for different devices

## Slide 27: General overview – ZAXPY in OpenMP
double x[N], y[N], z[N], a; //calculate z[i]=a*x[i]+y[i]
#pragma omp parallel for
for (int i=0; i<N; i++)
z[i] = a*x[i] + y[i];
Multicore

## Slide 28: General overview – ZAXPY in OpenMP
Code is unmodified except for the pragma
Data (x, y, z, a) is implicitly copied
Calculation done on device if available
  Runs on CPU otherwise
double x[N], y[N], z[N], a; //calculate z=a*x+y
#pragma omp target
{
for (int i=0; i<N; i++)
z[i] = a*x[i] + y[i];
}
Offloading
Compiler: Generate code for GPU
Runtime: Run code on device if possible, copy data from/to GPU

## Slide 29: OpenMP offloading – distributing work
By default, code in target region runs sequentially on accelerator
teams directive – create thread teams to perform work
  e.g., one team per SM of GPU
distribute parallel for:
  distribute for loop iterations among threads
Can be combined, as in the example above
double x[N], y[N], z[N], a; //calculate z=a*x+y
#pragma omp target
{
#pragma omp teams distribute parallel for
for (int i=0; i<N; i++)
z[i] = a*x[i] + y[i];
}

## Slide 30: OpenMP offloading – data movement
Data movement can be made explicit
  Data can be reused by multiple regions
double x[N], y[N], z[N], a;
#pragma omp target data map(tofrom: x[:N],y[:N],z[:N],a)
{
#pragma omp target
//[...]
#pragma omp target
//[...]
}
Copy data to device on entering region, copy it back to host on leaving region

## Slide 31: Programming GPGPUs:
CUDA
  High performance
  Control
  Can automate data movement
OpenMP Target
  Automates Data Movement
  “Easy”
cuLibraries : cuBLAS, cuFFT, etc
  Very high performance/tuned
  Drop in replacement
Others: OpenCL, OpenACC, etc

## Slide 32: Resources and Further Reading
Courses
  MCSDS
  Coursera(?)
Books
  Wen-Mei Hwu and David Kirk
  Others
Nvidia’s CUDA Programming Guide: docs.nvidia.com/cuda/
Managed Memory
Streams
Optimizations
  Bank conflicts
  Shared memory