## Slide 1: Memory Access Challenges
Performance Impact of Caches

## Slide 2: Recall: Cache Hierarchies and Performance
CPU
Memory
Cache
Cache is fast memory, typically on chip
  DRAM is off-chip
It has to be small to be fast
It is also more expensive than DRAM on per-byte basis
Idea: bring frequently accessed data in the cache

## Slide 3: Why and How Does a Cache Help?
Temporal and spatial locality
  Programs tend to access the same and/or nearby data repeatedly
Size of cache
Multiple levels of cache
Performance impact of caches
  Designing programs for good sequential performance
Notes: 3

## Slide 4: Cache: Parameters and Metrics
Cache line: spatial locality
  64 bytes or 128 bytes, consecutive memory addresses
  Make it too short: what happens?
  Make it too long: what happens?
Hit ratio
  Fraction of times a data item is found in cache
  Best possible: 1
  May be higher than that given by reuse ratio because of spatial locality

## Slide 5: Cache: Parameters and Metrics
Cache line: spatial locality
  64 bytes or 128 bytes, consecutive memory addresses
  Make it too short: what happens? Too many cache misses, ..
  Make it too long: what happens? Potential waste if not that much spatial reuse
Hit ratio
  Fraction of times a data item is found in cache
  Best possible: 1
  May be higher than that given by reuse ratio because of spatial locality

## Slide 6: Cache Mapping and Associativity
Say you have 64 KB of cache, 64 byte cache lines
  So, 1024 cache blocks in all
On a read miss, you have to fetch a cache line from memory
  (Or from next level cache)
  Where in the cache should it go?
    I.e., which of the 1024 blocks should be used to store it?
    A fixed place based on the address: direct-mapped cache
    Anywhere: fully-associative cache
      Expensive (hardware and time!)
Solution: Set associative cache

## Slide 7: Set Associative Cache
Set associative: 4 sets of 2 cache lines each
Program’s memory: a sequence of cache lines
Where in the cache can the shaded one go
(if it needs to be brought into the cache)?
Fully associative
Direct mapped
0
63
64

## Slide 8: Cache Replacement Policy
Which cache line to evict?
For direct mapped cache, there is only one candidate
For associative caches, multiple choices exist, so a policy is needed
  Random
  LRU: least recently used
  What do you think will be a good policy?
  But no significant impact on performance across applications is observed…

## Slide 9: Categorizing Cache Misses
Compulsory misses:
  “Cold” cache accesses, i.e., first time you access it
Capacity misses:
  There is no space in cache
Conflict misses:
  There is space, but it is not in the right set
The idea of a “working set”
  A set of addresses that the program accesses over a time window
Question: Which misses cannot happen with fully associative cache?
Conflict misses

## Slide 10: Example
for (i = 0; i < n; i += M ) // M is the cache-line size in words
A[i] = B[i] + C[i];
What happens with:
  Direct map cache?
  Fully associative cache?
  4-way associative cache?
How many cache misses?
What if the loop repeats?
  I.e., there is an outer loop
  Working set: the data in A, B, and C

## Slide 11: Another Example
for (i = 0; i < n; i++). sum = sum + A[i];
How many cache misses?
What kind of misses are those?
Can we reduce the cost of those misses? How?
Answers:
  One for every cache line... N/k, where k is the size of a cache line in words
    So, 64 byte cache line, single precision words of 4 bytes: k = 16
These are all compulsory misses
    First time we access the data
Notes: Eg if n is 32million, 2m misses

## Slide 12: Example Program
Imagine a sequential program running using a large array, A
For each I, A[i] = A[i] + A[some other index]
Values in the indirection array are all between 0…size-1
How long should the program take, if each addition is a ns?
What is the performance difference you expect, depending on the value of size?
for (i = 0; i < repetitions/size; i++)
for (count1 =0; count1 < size ; count1++) {
A[count1] += A[ indirection[count1] ]; }
Notes: 12