## Slide 1: Other Architectural Innovations
© 2018 L. V. Kale at the University of Illinois Urbana-Champaign

## Slide 2: Prefetch
Look for pattern in memory accesses:
  That you are accessing successive memory locations in A
  If I make the hardware detect this pattern, what can I do?
Two techniques:
  Bring multiple cache lines in on a miss
  Prefetch even more lines… asynchronous load instructions

## Slide 3: Out of Order Execution
Keep many instructions “in flight”
If there are data dependencies, buffer the instruction
Important techniques: Register renaming, scoreboarding, etc., to satisfy dependencies and ensure correctness
Also, try to issue multiple instructions per cycle!

## Slide 4: Superscalar Processors
Can we execute multiple instructions per cycle?
  FMAD was a single instruction
Idea: Fetch multiple instructions in each cycle…
  And execute as many of them in parallel as is possible without violating data dependencies
  Need more hardware on chip
  More registers for buffering results
  Multiple load units, etc.
IPC: instruction-level parallelism
  How many can you execute in each cycle?
  Typically 2-3 is the max

## Slide 5: Impact on programming
Usually, we should let the compiler handle this
But its useful to know whether our program is exploiting the superscalar processors well
  IPC : instructions per cycle --- this is a useful metric to track
Try to write code such that consecutive instructions can be executed concurrently
  Avoid dependences.. But these may be unavoidable
  ILP (Instruction level parallelism)
Avoid pipeline bubbles