## Slide 1: Shared Memory Multiprocessors
Multiple Processors Accessing a Common Memory
© 2018 L. V. Kale at the University of Illinois Urbana-Champaign

## Slide 2: Shared Memory Multiprocessor and Caches
…
Processors
CPU0
CPU1
CPUk-1
Memory (DRAM)
Cache
X: 5
Load X
Cache Controller
Cache
Cache
Cache Controller
Cache Controller
X: 7
X: 5
Load X
Load X
X: 5
Store X, 7
Notes: Make the animated portions in different color (all the X:5 X:7 texts, and the Load X instructions)

## Slide 3: Cache Coherence, Snoopy Caches, and MSI Protocol
The cache controllers watch every transaction on the bus
  Even if its not their transaction ... hence “snoopy”
Each cache line is in one of three states:
  M: Modified - my copy is “dirty” (i.e., up to date) ... don’t let others use the stale copy from the DRAM
  S: Shared - I have a copy, and I know others have a copy, and none of them is M
  I: Invalid - I have a copy, but another processor’s cache has a later version. Don’t let my processor use my copy

## Slide 4: The Illinois Protocol (a.k.a. MESI Protocol)
Prof. Janak Patel et. al
Each cache line is in one of four states:
  M: Modified
  E: Exclusive: I have a copy, no other caches have a copy and it is clean
    i.e. same as the copy in DRAM
  S: Shared: I have a copy; I know others have a copy, and none of them is M
  I: Invalid
Each cache controller monitors transactions on the shared bus
  Snooping

## Slide 5: Shared Memory Multiprocessor and Caches
…
Processors
CPU0
CPU1
CPUk-1
Memory (DRAM)
Cache
X: 5
Load X
Cache Controller
Cache
Cache
Cache Controller
Cache Controller
X: 7
X: 5
Load X
Load X
X: 5
Store X, 7

## Slide 6: Real Cache Coherence Hardware
Real cache coherence hardware is more complex than that
Instead of a single shared bus, a complex interconnect
L1, L2, L3 Caches
Shared caches:
  L1 typically private to a core (or two)
  SMT: symmetric multi-threading
    So, a core is typically multiple (2 or 4) hardware threads (hyperthreads)
  L3 is typically shared

## Slide 7: Performance Take-Aways (Lessons)
Cache traffic “serving” latest versions of cache lines can be a bottleneck
  Bus traffic
Data written by one core and read by another core(s) causes cache traffic
  This is based on the cache line, not a variable
  I.e., if you “load X”, not just the 4 bytes of X, but the surrounding 32 (say) bytes of a cache-line have to be moved from a neighboring core’s cache to yours (or from the DRAM)